## Slide 1: Small Distributed Generation Interconnection & Net Billing
Commission Information Update
October 27, 2026

## Slide 2: What Has Changed Since September 8?
SEP 8
Initial Commission briefing
Identified technical, document, rate and governance work.
SINCE THEN
Documents + Project advance
District document development; Continued coordination with customer;
OCT 27
Information update
Share draft application, agreement approach, and Net Billing rate structure.
NOV
Commission rate action
Staff intends to return with a final recommendation on the Net Billing rate schedule
CURRENT PROJECT STATUS
200 kW AC
Final proposed Maximum Generating Capacity
Engineering review
Existing Resolution 2259 (Tier 2) provides the technical basis to continue
Customer ready
Customer preparing for procurement and construction;
BPA coordination
Confirmed BPA rules not applicable, when less than or equal to 200 kW AC

## Slide 3: Generation Capacity Size Thresholds
200 kW AC
PROJECT
Different thresholds answer different questions regarding:
Technical interconnection, billing eligibility, BPA transmission processes, and BPA power-supply treatment.
3
100 kW
25 kW
200 kW
500 kW
1 MW
20 MW
SCHEMATIC — THRESHOLDS NOT TO SCALE
≤ 100 kW
net-metering size limit
WA NET METERING
RCW 80.60
> 0.2 MW to ≤ 20 MW
BPA Small Generator Interconnection Procedures (SGIP), where applicable
BPA TRANSMISSION
Small Gen. Procedures
Regional Dialogue:
Resources ≤ 200 kW not required to be dedicated
Provider of Choice:
Resource threshold increases to ≤ 1 MW
BPA POWER
RD → Provider of Choice
BPUD PROCESSES
Net Metering / Net Billing
≤ 100 kW,
Net Metering (Existing)
≤ 200 kW,
Net Billing (New)
Tier 3, < 20 MW,
project-specific review as applicable
WAC 480-108-020 Provides a similar framework for UTC-regulated utilities but does not govern BPUD.
BPUD Interconnection Standards
Resolution #2259
Tier 1,
≤ 25 kW
Tier 2, < 500 kW,
with screens met
BPUD Net Metering Interconnection Standards
Tier 1,
≤ 25 kW
Tier 2,
≤ 100 kW

## Slide 4: A Repeatable Customer-Facing Framework Is Taking Shape
1
Interconnection Application
Defines the project
Project’s “Maximum Generating Capacity”
Utility’s “Applicable Interconnection Standards”
2
Engineering Review
Confirms what is required
Review Project Application
Identify project-specific requirements and costs
4
Net Billing Rate Schedule
Defines compensation
3
Interconnection Agreement
Defines the obligations
Approved Interconnection Application becomes ATTACHMENT A
References the Net Billing Rate Schedule
Utility’s Applicable Interconnection Standards become ATTACHMENT B
Project-specific requirements & costs, if any, become
ATTACHMENT C
Retail purchases remain on retail rate
Imports and exports separately metered
Excess generation credited at the avoided cost rate
Avoided cost rate set by Commission
Avoided cost rate subject to change

## Slide 5: Near-Term Path to Move the Project Forward
Complete
technical review
Confirm the project-specific interconnection requirements.
Finalize
customer documents
Complete the application and execute the agreement.
Commission adopts Net Billing rate schedule
Approve the generation credit and net billing implementation.
Resolve Remaining
Questions
Review any Interconnection Agreement and net billing questions.
Today’s emphasis is the near-term path to move this project forward.
Broader document updates may follow later.

## Slide 6: BPA Load Following Contract

## Slide 7: 2027 Gross Power Supply Cost by Source
Chart: 
| Net Conservation | BPA Preliminary Injunction | BPA Demand | Renewables & Other | BPA Tier 1 Power | BPA Tier 1 Load Shaping Charge/(Credit) | BPA Tier 2 | BPA Transmission | Ancillary Services
Expenditures | 0.4 | 5.4 | 4.6 | 5 | 56.7 | 0.6 | 6.9 | 11.1 | 1.6
Column1 | 0.0043337 | 0.058505 | 0.049837 | 0.054171 | 0.6143 | 0.0065005 | 0.074756 | 0.12026 | 0.017335
Description | Amount
BPA Tier 1 Power | $56.7
BPA Tier 1 Load Shaping Charge/(Credit) | 0.6
BPA Tier 2 Power | 6.9
BPA Demand | 4.6
BPA Preliminary Injunction (BP-27) | 5.4
BPA Transmission | 11.1
Renewables & Other | 5.0
Ancillary | 1.6
Net Conservation | 0.4
Gross Power Supply | $92.3
Less: Secondary Market Sales | (1.5)
Less: Transmission Sales | (0.1)
Net Power Expense | $90.7
Gross Power Supply $92.3 million
Dollars in millions

## Slide 8: BPA Rates: Tier 1 v. Tier 2
Follows Load
Flat Block
Above CHWM =

## Slide 9: Benton PUD’s Resource Plan
BPA Tier 1 CHWM increases to 213.007 aMW effective 10/1/2028
16-Year Provider of Choice Contract

## Slide 10: BPA Rates: Tier 1 v. Tier 2
Tier 2 Rate
  Forecast Net Requirement above CHWM Fixed Cost for BPA Rate Period
  Fixed also referred to as “Take-or-Pay”
Tier 1 Rate
  Tier 1 Composite/Non-Slice Rate Fixed Cost for BPA Rate Period
    Based on lower of Contract High Water Mark (CHWM) or Forecast Net Requirement
  Load Shaping Rate Variable Cost during BPA Rate Period
    This rate “trues-up” actual load to forecast load during a BPA rate period
    ~$40/MWh on average

## Slide 11: BPA Rates: Tier 1 v. Tier 2
2024
2025
2026
2027
2028
2029
2030
Fiscal Year
BP-24
Rate Case
BP-26
BP-29
Forecast Net Requirement Finalized For BP-26
Forecast Net Requirement Finalized For BP-29

## Slide 12: BPA Rates: BP-26 Tier 1 v. Tier 2
Chart: 
| Total Retail Load | Resources | Total Retail Load | Resources | Total Retail Load | Resources | FY2026 | FY2027 | FY2028
BPA Tier 2 | 10.666 | 11.564 | 11.74
Packwood* | 0.919 | 0.919 | 0.919
BPA Tier 1 (RHWM) | 202.081 | 202.081 | 202.081
TRL | 213.666 | 214.564 | 214.739
*Packwood is a dedicated resource at .92 aMW
Determined each Rate Case based on BPUD Load Forecast
BPUD gets 2.842% of Tier 1 power (Tier 1 Costs Allocator or TOCA). ~$35/MWh
Tier 2 = TRL – Tier 1 – Packwood. This amount is set for each Rate Case. ~$70/MWh
Once a BPA rate case is final, we know with precision how much we will pay for Tier 1 and Tier 2 every month of the rate case
Notes: Note: RPS has a cost cap
Per BPA Website the Tier 1 average rate is $37.77, but Benton PUD’s rate is $35.00 per the Rate Impact Model

## Slide 13: Load Shaping
Intended to charge or credit a customer based on how loads align with Tier 1 firm capability
BPA publishes monthly HLH and LLH load shaping rates in each rate case
  Based on forward market monthly amounts (separate process from Tier 2)
Load shaping also trues-up the difference from Tier 1 & Tier 2 “Take or Pay” rates established by forecast to actual load
The Load Shaping rate is Benton PUD’s marginal cost of energy during a BPA rate period

## Slide 14: Load Shaping Cost Example HLH
Chart: Example of Monthly HLH (aMW)
| 46296 | 46327 | 46357 | 46388 | 46419 | 46447 | 46478 | 46508 | 46539 | 46569 | 46600 | 46631
HLH Load Shaping Charge/(Credit) | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0
BPA Tier 1 Shape | 170.1514 | 237.2803 | 264.2123 | 285.0739 | 238.9118 | 237.2744 | 180.7865 | 239.3023 | 252.9482 | 218.8964 | 235.554 | 178.15
BPUD Tier 1 Load | 157.1473 | 182.11 | 203.3169 | 213.449 | 187.4907 | 154.1817 | 164.9111 | 216.9334 | 276.0193 | 324.5863 | 293.34 | 197.7341
BPA Load Shaping Rates by Month
~$40/MWh average
Notes: BP-26 Load Shaping rates
Oct & Apr ID’d as constraints in BPA Resource Study

## Slide 15: Load Shaping Cost Example HLH
Chart: Example of Monthly HLH (aMW)
| 46296 | 46327 | 46357 | 46388 | 46419 | 46447 | 46478 | 46508 | 46539 | 46569 | 46600 | 46631
HLH Load Shaping Charge/(Credit) | -284428 | -837458 | -1206588 | -1247992 | -897048 | -1047806 | -147471 | -76949 | 144924 | 2241438 | 1293297 | 474013
BPA Tier 1 Shape | 170.1514 | 237.2803 | 264.2123 | 285.0739 | 238.9118 | 237.2744 | 180.7865 | 239.3023 | 252.9482 | 218.8964 | 235.554 | 178.15
BPUD Tier 1 Load | 157.1473 | 182.11 | 203.3169 | 213.449 | 187.4907 | 154.1817 | 164.9111 | 216.9334 | 276.0193 | 324.5863 | 293.34 | 197.7341
Total HLH Load Shaping = $(1,592,068)
BPA Load Shaping Rates by Month
~$40/MWh average
Notes: BP-26 Load Shaping rates
Oct & Apr ID’d as constraints in BPA Resource Study

## Slide 16: Load Shaping Cost Example HLH
Chart: Example of Monthly HLH (aMW)
| 46296 | 46327 | 46357 | 46388 | 46419 | 46447 | 46478 | 46508 | 46539 | 46569 | 46600 | 46631
HLH Load Shaping Charge/(Credit) | -169578 | -754465 | -1104426 | -1156331 | -806522 | -982763 | -98492 | -57906 | 178124 | 2353798 | 1418158 | 605256
BPA Tier 1 Shape | 170.1514 | 237.2803 | 264.2123 | 285.0739 | 238.9118 | 237.2744 | 180.7865 | 239.3023 | 252.9482 | 218.8964 | 235.554 | 178.15
BPUD Tier 1 Load | 162.3983 | 187.5774 | 208.4729 | 218.7096 | 192.6799 | 159.3398 | 170.1838 | 222.4692 | 281.3047 | 329.8844 | 298.9189 | 203.1564
Total HLH Load Shaping = $(575,147)
BPA Load Shaping Rates by Month
~$40/MWh average
Increase Load 5 aMW
Notes: BP-26 Load Shaping rates
Oct & Apr ID’d as constraints in BPA Resource Study

## Slide 17: Load Shaping Cost Example HLH
Chart: Example of Monthly HLH (aMW)
| 46296 | 46327 | 46357 | 46388 | 46419 | 46447 | 46478 | 46508 | 46539 | 46569 | 46600 | 46631
HLH Load Shaping Charge/(Credit) | -399279 | -920451 | -1308749 | -1339653 | -987573 | -1112850 | -196450 | -95992 | 111724 | 2129079 | 1168436 | 342771
BPA Tier 1 Shape | 170.1514 | 237.2803 | 264.2123 | 285.0739 | 238.9118 | 237.2744 | 180.7865 | 239.3023 | 252.9482 | 218.8964 | 235.554 | 178.15
BPUD Tier 1 Load | 151.8963 | 176.6426 | 198.1609 | 208.1884 | 182.3015 | 149.0236 | 159.6385 | 211.3976 | 270.734 | 319.2883 | 287.761 | 192.3117
Total HLH Load Shaping = $(2,608,987)
BPA Load Shaping Rates by Month
~$40/MWh average
Decrease Load 5 aMW
Notes: BP-26 Load Shaping rates
Oct & Apr ID’d as constraints in BPA Resource Study

## Slide 18: Avoided Cost
If BPA Tier 1 Composite & Tier 2 are “take or pay”; and
Benton PUD’s Tier 2 exposure is ZERO for BP-29,
What is the avoided energy cost to Benton PUD from customer owned distributed generation?
  BPA’s Load Shaping rate
If Benton PUD had Tier 2 exposure for BP-29, what is the avoided energy cost?
  Mostly BPA’s Tier 2 rate, with some Load Shaping

## Slide 19: Net Billing & Avoided Cost Credit Development

## Slide 20: How Net Billing Would Work
IMPORTS from Benton PUD
Customer purchases all energy physically flowing from Benton PUD under the applicable retail rate schedule (e.g., Medium General Service).
EXPORTS to Benton PUD
Excess generation receives a bill credit under a separately published, Commission-approved, Net Billing rate schedule (e.g. avoided cost)
KEY POINT | Imported and exported energy are measured separately; only exports receive the avoided-cost credit
3. Customer uses solar power
Solar generation consumed on-site reduces energy purchased from
Benton PUD.

## Slide 21: Proposed Avoided-Cost Credit
4.0352¢ per kWh
3.7166¢
per kWh
Avoided BPA Energy
Load Shaping Rates
0.1267¢
per kWh
Avoided Benton PUD
Transmission & Distribution
Losses
0.1919¢
per kWh
Avoided Renewable
Energy Certificate Purchases

## Slide 22: How Staff Developed the Avoided BPA Load Shaping Rate
Used NREL’s PVWatts calculator to develop an hourly solar production profile for our service territory and apply BPA’s hourly load shaping rates to calculate the avoided cost.
Method
NREL Solar Production Profile
(Kennewick, WA)
3.7166¢
per kWh
Avoided BPA Energy
Load Shaping Rates
Notes: 3.9388¢ if we wanted to use the average load shaping charge

## Slide 23: How Staff Developed the Benton PUD T&D Loss Rate
Line losses are the electricity lost as it travels through Benton PUD’s transmission and distribution system before reaching the customer.
0.1267¢
per kWh
Avoided Benton PUD
T & D Losses
Notes: Benton PUD's Transmission and Distribution (T&D) loss rate calculation estimates the additional electricity the District must purchase to account for energy lost as it travels through its electrical system before reaching customers.
By generating electricity locally, customers can reduce the amount of electricity that would otherwise need to travel through Benton PUD's system, avoiding some of those losses.
Step 1: Determine Benton PUD's T&D loss percentage
Based on the District's historical loss calculations, staff used a 10-year average T&D loss rate of 3.30%.
This means that for every 100 kWh entering the District's distribution system, approximately 96.7 kWh reaches customers.
Step 2: Calculate the electricity required to deliver 1 kWh
Because some electricity is lost during delivery, Benton PUD must purchase more than 1 kWh to deliver 1 kWh to a customer.
Step 3: Adjust the avoided energy cost
Staff calculated an avoided BPA energy cost of 3.7166¢ per kWh.
To account for Benton PUD's T&D losses, multiply this rate by the amount of electricity required to deliver 1 kWh.
Step 4: Calculate the avoided T&D loss component
Subtract the original avoided energy rate from the adjusted rate.

## Slide 24: How Staff Developed the Avoided REC Purchase Rate
1
Select REC Contract
Use the most recent contract reflecting the current REC market (3 Degrees – 2026).
$12.79
per REC
2
Apply EIA Requirement
Multiply the selected REC price by the 15% EIA requirement.
$12.79
per REC
×
15%
=
$1.9185
per MWh
3
Convert to ¢/kWh
Divide $/MWh by 10 to convert to cents per kWh.
$1.9185
per MWh
÷
10
=
0.1919¢
per kWh
0.1919¢
per kWh
Avoided
REC Purchases
Notes: The reason Benton PUD multiplies the cost per Renewable Energy Certificate (REC) by the Energy Independence Act (EIA) requirement of 15% is that the District does not need to purchase one REC for every MWh of electricity it sells. It only needs enough qualifying renewable energy or RECs to satisfy its 15% renewable energy requirement.

## Slide 25: Draft Schedule 91: Net Billing for Small Distributed Generation
Customer self-consumption reduces retail purchases but does not earn a separate generation credit.
Key Takeaways
Annual Settlement – March 31
Balances of $500 or more: customer may request payment or carry forward. Balances below $500: automatically carry forward.
Monthly Credits
Generation credits apply after retail charges are calculated. Unused monetary credits carry forward to future bills.
Generation Credit
4.04¢/kWh for energy delivered to the District. Rate Schedule requires a review of the avoided-cost rate for each BPA rate period.
Net Billing
Retail charges apply to electricity received from Benton PUD. Excess electricity exported to the District earns a separate credit.
Eligibility
Generation greater than 100 kW AC and not more than 200 kW AC; on customer premises with an executed interconnection agreement.

## Slide 26: Next Steps
October 27, 2026
Information & Discussion
Presented proposed Schedule 91 concepts and avoided cost methodology; receive Commission feedback
November 2026
Commission Approval
Staff returns with final Schedule 91
and a resolution for Commission consideration
Project Execution
Interconnection Agreement
Complete the project interconnection application and execute the agreement
No Commission action requested today

## Slide 27: Other Avoided Cost Components Evaluated
Guiding Principle: Include only costs that reduce Benton PUD’s actual expenses when
customer generation is delivered to the District, while avoiding double compensation.
BPA Tier 2
Excluded currently – Existing power commitments and anticipated Tier 1 headroom limit incremental savings from customer generation
Demand & Capacity
Excluded – Net billing already allows customers to reduce retail demand charges. Additional capacity savings were not established.
BPA Rate Adjustments
Excluded – COORA, FRP, CRAC, and RDC are generally based on fixed billing determinants rather than actual loads.
Transmission & Infrastructure
Excluded – Non demonstrated reduction in BPA transmission billing demand or deferral of specific capital projects.
Other Potential Avoided Costs
Social cost of carbon, risk adders, ancillary services and resource adequacy were evaluated but excluded because they do not represent separately identifiable, directly avoided District costs under this methodology.

## Slide 28: How Staff Developed the Benton PUD T&D Loss Rate
Notes: This slide is deliberately conceptual. Jon can first explain how BPA billing works, then use these categories to explain why an avoided-cost credit is different from both the retail rate and a wholesale market price. Components remain subject to analysis. [Sources] • Draft Retail Electric Rate Schedules Attachment Use this one (no EIL rates).docx — working Schedule 91 • Benton PUD internal Net Billing design discussion; current BPA Load Following / power-supply context

## Slide 29: How Staff Developed the Avoided BPA Load Shaping Rate
Use NREL’s PVWatts calculator to develop an hourly solar production profile for our service territory and apply BPA’s hourly load shaping rates to calculate the avoided cost.
Assume 1 kW of generation in every hour and apply BPA’s hourly load shaping rates to calculate the avoided cost.
3.7166¢
3.9388¢
Notes: This slide is deliberately conceptual. Jon can first explain how BPA billing works, then use these categories to explain why an avoided-cost credit is different from both the retail rate and a wholesale market price. Components remain subject to analysis. [Sources] • Draft Retail Electric Rate Schedules Attachment Use this one (no EIL rates).docx — working Schedule 91 • Benton PUD internal Net Billing design discussion; current BPA Load Following / power-supply context

## Slide 30: Load Shaping Cost Example LLH
Chart: Example of Monthly LLH (aMW)
| 46296 | 46327 | 46357 | 46388 | 46419 | 46447 | 46478 | 46508 | 46539 | 46569 | 46600 | 46631
LLH Load Shaping Charge/(Credit) | -70937 | -429241 | 13158 | -78019 | -163461 | -377909 | -92317 | -54797 | 264403 | 1908152 | 1166965 | 488944
BPUD Tier 1 Load | 137.8519 | 146.5679 | 188.4881 | 189.2442 | 170.499 | 142.0038 | 143.1973 | 168.7583 | 239.0469 | 281.5562 | 221.3972 | 160.9575
BPA Tier 1 Shape | 142.5062 | 177.1565 | 187.6659 | 194.4222 | 182.0397 | 177.1846 | 154.4072 | 181.2714 | 184.9582 | 160.5088 | 150.6933 | 135.0864
Total LLH Load Shaping = $2,574,941